AUTOMATED FIRE EXTINGUISHING SYSTEM

Minor Report
2016-2017

Submitted to:	Submitted by:
Mrs. Hema N	Supriya Sahu
       14103057	B-10

Problem Statement:

In the present project the development of automated fire extinguisher signifies to control and prevent the fire in wild forest as well as commercial and residential complexes in the entire human community. This type of emerging robotic technology would help to save the life of human beings and also help to conserver the wild community without any severe economic losses. The robotic system to extinguish the fire in a residential area including the commercial places is better than the present smoke detectors along with the water sprinklers and chemical process.

What all does the project include?
1-I2C is used.

2-Djikstra Algorithm to reach the destination via shortest path.
3-Thermal and flame Sensors
4-Arduino Mega which act as server and arduino unos which act as slaves. Mega will define the path and required number of slaves will go to the affected destination via shortest path.
Detailed description of components and algorithm

Thermal Sensors – If a person is not available to give instruction using iot, these sensors will sense the fire and will call server arduino for help.

Flame sensor-Detects the intensity of fire.

Arduino Mega and Arduino Uno - Mega act as server and unos act as slaves. Mega will define the path, send the path to appropriate unos[1 or more], direct them and required number of slaves will go to the affected destination via shortest path.

Djikstra Algorithm – The graph is given by user.Djikstra algorithm is used to find the shortest path.

SLAVE

int motorpin3 = 3; //motor1
int motorpin4 = 4; //motor2
int motorpin6 = 6; //motor3
int motorpin7 = 7; //motor4
int motorpin9 = 9; //motor for mechanism
int motorpin10 = 10; //motor for mechanism

const int TEST_PIN = 10;
int s,d,i,x,y,r,m,j;
char arrdir[13][13] ={ //0 1 2 3 4 5 6 7 8 9 10 11 12
        {'a','s','a','a','a','a','a','a','a','r','a','a','a'}, //0
        {'a','a','s','a','r','a','a','a','a','a','a','a','a'}, //1
        {'a','a','a','s','a','r','a','a','a','a','a','a','a'}, //2
        {'a','a','a','a','a','a','a','a','r','a','a','a','a'}, //3
        {'a','a','a','a','a','s','a','a','a','a','a','a','a'}, //4
        {'a','a','a','a','a','a','a','a','a','a','a','a','a'}, //5
        {'a','a','a','a','a','a','a','s','a','a','a','a','a'}, //6
        {'a','a','a','a','a','a','a','a','a','s','a','r','a'}, //7
        {'a','a','a','a','a','a','a','a','a','a','a','a','a'}, //8
        {'a','a','a','a','a','a','a','a','a','a','s','a','a'}, //9
        {'a','a','a','a','a','a','l','a','a','a','a','a','a'}, //10
        {'a','a','a','a','a','a','a','a','a','a','a','a','s'}, //11
        {'a','a','a','a','a','a','a','a','a','a','a','a','a'} //12
        };

int arrdist[13][13]={// 0 1 2 3 4 5 6 7 8 9 10 11 12
        {0,1,0,0,0,0,0,0,0,3,0,0,0}, //0
        {0,0,1,0,1,0,0,0,0,0,0,0,0}, //1
        {0,0,0,1,0,1,0,0,0,0,0,0,0}, //2
        {0,0,0,0,0,0,0,0,10,0,0,0,0}, //3
        {0,0,0,0,0,1,1,0,0,0,0,0,0}, //4
        {0,0,0,0,0,0,0,0,0,0,0,0,0}, //5
        {0,0,0,0,0,0,0,1,0,0,0,0,0}, //6
        {0,0,0,0,0,0,0,0,0,1,0,1,0}, //7
        {0,0,0,0,0,0,0,0,0,0,0,0,0}, //8
        {0,0,0,0,0,0,0,0,0,0,1,0,0}, //9
        {0,0,0,0,0,0,1,0,0,0,0,0,0}, //10
        {0,0,0,0,0,0,0,0,0,0,0,0,1}, //11
        {0,0,0,0,0,0,0,0,0,0,0,0,0} //12
        };

static int count1 = 0;
int arrpath[20];
static int arr[10];
static int count = 0;
int xxxx= 0;

void setup() {
  Serial.begin(9600); // start serial for output
  pinMode(motorpin3,OUTPUT); //set pin 3 as output
  pinMode(motorpin4,OUTPUT);
  pinMode(motorpin6,OUTPUT); //set pin 3 as output
  pinMode(motorpin7,OUTPUT);
  pinMode(motorpin9,OUTPUT); //set pin 3 as output
  pinMode(motorpin10,OUTPUT);
    y=0;
  Wire.begin(8); // join i2c bus with address #8
  Wire.onReceive(receiveEvent); // register event

for(int i = 0; i < count ; i++)
    {
     Serial.print(arrpath[i]);
    }

Serial.println("now you can proceed");
}

void loop() {

  if(xxxx-1 == arr[count-1]+1)
{

    //for(i =0 ; i< count ; i++)
     //Serial.println(arr[i]);

  Serial.print("the path of xxxx is :: ");

for(int i = 0 ; i < count-1 ; i++)
   {
       digitalWrite(3,LOW);
       digitalWrite(4,LOW);
       digitalWrite(6,LOW);
       digitalWrite(7,LOW);

     delay(5000);
     if(i == 0)
     {
        if(arrdir[arr[i]][arr[i+1]] == 'r')
        {
        arrpath[count1] = arrdir[arr[i]][arr[i+1]]; //------move ye 1st hai
        Serial.println(arrpath[count1++]);

        //code for movee
        digitalWrite(3,HIGH);
        digitalWrite(4,LOW);
        digitalWrite(6,LOW);
        digitalWrite(7,LOW);
        delay(650);

        }

        arrpath[count1] = arrdir[arr[i]][arr[i+1]]; //------move ye 1st hai
        Serial.println(arrpath[count1++]);

       //code for movee
        digitalWrite(3,HIGH);
        digitalWrite(4,LOW);
        digitalWrite(6,HIGH);
        digitalWrite(7,LOW);
        delay(arrdist[arr[i]][arr[i+1]] * 1000);
        continue;

   }
     else{

    if(arrdir[arr[i]][arr[i+1]] == 's' && arrpath[count1 - 1] == 's') // move
     {
       arrpath[count1] = 's';
        Serial.println(arrpath[count1++]);

       digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);
       delay(arrdist[arr[i]][arr[i+1]] * 1000);

        continue;

     }

     else if(arrdir[arr[i]][arr[i+1]] == 'r' && arrpath[count1 - 1] == 's') //-----just rotate and move //ye 2nd hai
     {
       arrpath[count1] = 'r';
        Serial.println(arrpath[count1++]);

       //code for rotate in right
       digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,LOW);
       digitalWrite(7,LOW);
       delay(650);
       //code for move
       digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);
       delay(arrdist[arr[i]][arr[i+1]] * 1000);
      continue;

     }

     else if(arrdir[arr[i]][arr[i+1]] == 'l' && arrpath[count1 - 1] == 's') //just rotate
     {
       arrpath[count1] = 'l';
        Serial.println(arrpath[count1++]);

       digitalWrite(3,LOW);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);
       delay(650);

  //move
        digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);

      delay(arrdist[arr[i]][arr[i+1]] * 1000);
      continue;

     }

    else if(arrdir[arr[i]][arr[i+1]] == 'r' && arrpath[count1 - 1] == 'r') //just straight
     {
       arrpath[count1] = 's';
       Serial.println(arrpath[count1++]);

       digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);

      delay(arrdist[arr[i]][arr[i+1]] * 1000);
      continue;

     }

    else if(arrdir[arr[i]][arr[i+1]] == 's' && arrpath[count1 - 1] == 'r') //------just rotate and move //ye 3rd hai
     {
       arrpath[count1] = 'l';
       Serial.println(arrpath[count1++]);

       //code for rotate
       digitalWrite(3,LOW);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);
       delay(650);
       //code for move
        digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);

     delay(arrdist[arr[i]][arr[i+1]] * 1000);
        continue;

     }

    else if(arrdir[arr[i]][arr[i+1]] == 's' && arrpath[count1 - 1] == 'l') //just rotate
     {
       arrpath[count1] = 's';
       Serial.println(arrpath[count1++]);
        digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);

     delay(arrdist[arr[i]][arr[i+1]] * 1000);

     }

     else if(arrdir[arr[i]][arr[i+1]] == 'l' && arrpath[count1 - 1] == 'l') //just rotate
     {
       arrpath[count1] = 'l';
       Serial.println(arrpath[count1++]);

        //code for rotate
       digitalWrite(3,LOW);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);
       delay(650);
       //code for move
        digitalWrite(3,HIGH);
       digitalWrite(4,LOW);
       digitalWrite(6,HIGH);
       digitalWrite(7,LOW);

   }

   }

       digitalWrite(3,LOW);
       digitalWrite(4,LOW);
       digitalWrite(6,LOW);
       digitalWrite(7,LOW);

}

for(int i = 0 ; i < 3 ; i++ )
{
digitalWrite(9,LOW);
       digitalWrite(10,HIGH);
       delay(1500);
       digitalWrite(10,HIGH);
       digitalWrite(9,LOW);
       delay(1500);

}

xxxx++;

}

/*
for(int i =0 ; i < 3 ; i++)
   {
       analogWrite(9,0);
       analogWrite(10,255);
       delay(5000);
       analogWrite(9,255);
       analogWrite(10,0);
\ delay(5000);
   }

*/
  delay(100);
}

// function that executes whenever data is received from master
// this function is registered as an event, see setup()

void receiveEvent(int howMany) {

  while (1 < Wire.available()) { // loop through all but the last
    char c = Wire.read(); // receive byte as a character
    Serial.print(c); // print the character
  }
  int x = Wire.read(); // receive byte as an integer
  arr[count++] = x;

  Serial.println(arr[count-1]); // print the integer

 xxxx++;

}

Modified implementaton of Djikstra:

struct AdjListNode

{
    int dest;
    int weight;
    struct AdjListNode* next;
};

struct AdjList
{
  struct AdjListNode *head; // pointer to head node of list
};

struct Graph
{
    int V;
    struct AdjList* array;
};

// A utility function to create a new adjacency list node

struct AdjListNode* newAdjListNode(int dest, int weight)
{

    struct AdjListNode* newNode = (struct AdjListNode*) malloc(sizeof(struct AdjListNode));
    newNode->dest = dest;
    newNode->weight = weight;
    newNode->next = NULL;
    return newNode;

}

// A utility function that creates a graph of V vertices

struct Graph* createGraph(int V)
{
  struct Graph* graph = (struct Graph*) malloc(sizeof(struct Graph));
  graph->V = V;

    // Create an array of adjacency lists. Size of array will be V
    graph->array = (struct AdjList*) malloc(V * sizeof(struct AdjList));

   // Initialize each adjacency list as empty by making head as NULL
    for (int i = 0; i < V; ++i)
        graph->array[i].head = NULL;

     return graph;
}

// Adds an edge to an undirected graph

void addEdge(struct Graph* graph, int src, int dest, int weight)
{
    // Add an edge from src to dest. A new node is added to the adjacency

    // list of src. The node is added at the begining

    struct AdjListNode* newNode = newAdjListNode(dest, weight);
    newNode->next = graph->array[src].head;
    graph->array[src].head = newNode;

    // Since graph is undirected, add an edge from dest to src also

   /* newNode = newAdjListNode(src, weight);
    newNode->next = graph->array[dest].head;
    graph->array[dest].head = newNode;*/
}

 // Structure to represent a min heap node

struct MinHeapNode

{

    int v;

    int dist;

};

// Structure to represent a min heap

struct MinHeap

{

    int size; // Number of heap nodes present currently

    int capacity; // Capacity of min heap

    int *pos; // This is needed for decreaseKey()

    struct MinHeapNode **array;

};

// A utility function to create a new Min Heap Node

struct MinHeapNode* newMinHeapNode(int v, int dist)

{

    struct MinHeapNode* minHeapNode =

        (struct MinHeapNode*) malloc(sizeof(struct MinHeapNode));

    minHeapNode->v = v;

    minHeapNode->dist = dist;

    return minHeapNode;

}

// A utility function to create a Min Heap

struct MinHeap* createMinHeap(int capacity)

{

    struct MinHeap* minHeap =

        (struct MinHeap*) malloc(sizeof(struct MinHeap));

    minHeap->pos = (int *)malloc(capacity * sizeof(int));

    minHeap->size = 0;

    minHeap->capacity = capacity;

    minHeap->array =

        (struct MinHeapNode**) malloc(capacity * sizeof(struct MinHeapNode*));

    return minHeap;

}

// A utility function to swap two nodes of min heap. Needed for min heapify

void swapMinHeapNode(struct MinHeapNode** a, struct MinHeapNode** b)

{

    struct MinHeapNode* t = *a;

    *a = *b;

    *b = t;

}

// A standard function to heapify at given idx

// This function also updates position of nodes when they are swapped.

// Position is needed for decreaseKey()

void minHeapify(struct MinHeap* minHeap, int idx)

{

    int smallest, left, right;

    smallest = idx;

    left = 2 * idx + 1;

    right = 2 * idx + 2;

    if (left < minHeap->size &&

        minHeap->array[left]->dist < minHeap->array[smallest]->dist )

      smallest = left;

    if (right < minHeap->size &&

        minHeap->array[right]->dist < minHeap->array[smallest]->dist )

      smallest = right;

    if (smallest != idx)

    {

        // The nodes to be swapped in min heap

        MinHeapNode *smallestNode = minHeap->array[smallest];

        MinHeapNode *idxNode = minHeap->array[idx];

        // Swap positions

        minHeap->pos[smallestNode->v] = idx;

        minHeap->pos[idxNode->v] = smallest;

        // Swap nodes

        swapMinHeapNode(&minHeap->array[smallest], &minHeap->array[idx]);

        minHeapify(minHeap, smallest);

    }

}

// A utility function to check if the given minHeap is ampty or not

int isEmpty(struct MinHeap* minHeap)

{

    return minHeap->size == 0;

}

// Standard function to extract minimum node from heap

struct MinHeapNode* extractMin(struct MinHeap* minHeap)

{

    if (isEmpty(minHeap))

        return NULL;

    // Store the root node

    struct MinHeapNode* root = minHeap->array[0];

    // Replace root node with last node

    struct MinHeapNode* lastNode = minHeap->array[minHeap->size - 1];

    minHeap->array[0] = lastNode;

    // Update position of last node

    minHeap->pos[root->v] = minHeap->size-1;

    minHeap->pos[lastNode->v] = 0;

    // Reduce heap size and heapify root

    --minHeap->size;

    minHeapify(minHeap, 0);

    return root;

}

// Function to decreasy dist value of a given vertex v. This function

// uses pos[] of min heap to get the current index of node in min heap

void decreaseKey(struct MinHeap* minHeap, int v, int dist)

{

    // Get the index of v in heap array

    int i = minHeap->pos[v];

    // Get the node and update its dist value

    minHeap->array[i]->dist = dist;

    // Travel up while the complete tree is not hepified.

    // This is a O(Logn) loop

    while (i && minHeap->array[i]->dist < minHeap->array[(i - 1) / 2]->dist)

    {

        // Swap this node with its parent

        minHeap->pos[minHeap->array[i]->v] = (i-1)/2;

        minHeap->pos[minHeap->array[(i-1)/2]->v] = i;

        swapMinHeapNode(&minHeap->array[i], &minHeap->array[(i - 1) / 2]);

        // move to parent index

        i = (i - 1) / 2;

    }

}

// A utility function to check if a given vertex

// 'v' is in min heap or not

bool isInMinHeap(struct MinHeap *minHeap, int v)

{

   if (minHeap->pos[v] < minHeap->size)

     return true;

   return false;

}

// A utility function used to print the solution

void printArr(int dist[], int n,int d,int path[100],int s)

{

lcd.setCursor(0,0);
lcd.print("EXTINGUISHER 8");

  int k,j=0,tmp,f=0,c=0,temp[100];

     k=d;

 //for(int i = 0 ; i<=10 ; i++)
   // Serial.println(path[i]);

    for (int i = 0; i < n; ++i)

    if(i==d)

       // Serial.print(dist[i]);

lcd.setCursor(0, 1);

        while(k!=s)

        {

        tmp=path[k];

        temp[j]=tmp;

        k=tmp;

        j++;

        c++;

        }

lcd.setCursor(0, 1);

        for(j=c-1;j>=0;j--)

        {

        Wire.beginTransmission(8); // transmit to device #8
        Wire.write("x is "); // sends five bytes
        Wire.write(temp[j]); // sends one byte
        Wire.endTransmission();
        lcd.print(temp[j]);
        lcd.print(" ");

        if(temp[j]==d)
        f=1;
        }

        if(f!=1){
   // Serial.println(d);
        Wire.beginTransmission(8); // transmit to device #8
        Wire.write("x is "); // sends five bytes
        Wire.write(d); // sends one byte
        Wire.endTransmission();
        lcd.print(d);
        lcd.print(" ");

        }

        Serial.println(c);
        Wire.beginTransmission(8); // transmit to device #8
        Wire.write("Total nodes are "); // sends five bytes
        Wire.write(c); // sends one byte
        Wire.endTransmission();

}

// The main function that calulates distances of shortest paths from src to all

// vertices. It is a O(ELogV) function

void dijkstra(struct Graph* graph, int src,int d)

{

    int V = graph->V;// Get the number of vertices in graph

    int dist[V]; // dist values used to pick minimum weight edge in cut

    int path[100];

    int z;
     int sum = 0;
    // minHeap represents set E

    struct MinHeap* minHeap = createMinHeap(V);

    // Initialize min heap with all vertices. dist value of all vertices

    for (int v = 0; v < V; ++v)

    {

        dist[v] = INT_MAX;

        minHeap->array[v] = newMinHeapNode(v, dist[v]);

        minHeap->pos[v] = v;

    }

    // Make dist value of src vertex as 0 so that it is extracted first

    minHeap->array[src] = newMinHeapNode(src, dist[src]);

    minHeap->pos[src] = src;

    dist[src] = 0;

    decreaseKey(minHeap, src, dist[src]);

    // Initially size of min heap is equal to V

    minHeap->size = V;

    // In the followin loop, min heap contains all nodes

    // whose shortest distance is not yet finalized.

    while (!isEmpty(minHeap))

    {

        // Extract the vertex with minimum distance value

        struct MinHeapNode* minHeapNode = extractMin(minHeap);

        int u = minHeapNode->v; // Store the extracted vertex number

        // Traverse through all adjacent vertices of u (the extracted

        // vertex) and update their distance values

        struct AdjListNode* pCrawl = graph->array[u].head;

        while (pCrawl != NULL)

        {

        int v = pCrawl->dest;

        // If shortest distance to v is not finalized yet, and distance to v

        // through u is less than its previously calculated distance

        if (isInMinHeap(minHeap, v) && dist[u] != INT_MAX &&

        pCrawl->weight + dist[u] < dist[v])

        {

        dist[v] = dist[u] + pCrawl->weight;

        path[v]=u;

        z=v;

        // update distance value in min heap also

        decreaseKey(minHeap, v, dist[v]);

        }

        pCrawl = pCrawl->next;

        }

    }

     Serial.print("Shortest distance is");
     Serial.print(dist[d]);

    // print the calculated shortest distances

  // printArr(dist, V,d,path,src);

}

const int TEST_PIN = 10;
int V=22,s,d,i,x,y,r,m,j;
struct Graph* graph;

void setup()
{
Serial.begin(9600);
graph = createGraph(V);

    addEdge(graph, 0, 1, 1);
    addEdge(graph, 0, 9, 3);

    addEdge(graph, 1, 2, 1);
    addEdge(graph, 1, 4, 1);

    addEdge(graph, 2, 3, 1);
    addEdge(graph, 2, 5, 1);

    addEdge(graph, 3, 8, 2);

    addEdge(graph, 4, 5, 1);

   // addEdge(graph, 4, 6, 1);
    addEdge(graph, 6, 7, 1);

    addEdge(graph, 7, 8, 1);
    addEdge(graph, 7, 11, 1);

    addEdge(graph, 9, 10, 1);

    addEdge(graph, 10, 6, 1);

    addEdge(graph, 11, 12, 1);

    s = 0;
    d = 4;
// Serial.println("SUPRIYA SAHU ");
  // Serial.println("SUPRIYA SAHU ");
  Wire.begin(8);

    lcd.begin(16, 2);
  // Print a message to the LCD.
  analogWrite(9,0);
  lcd.print("hello, world!");

}
float temp;
int tempPin = A0;
static int count = 0;
void loop()
{
   temp = analogRead(tempPin);
   temp = temp * 0.48828125;
   if(temp > 25.00)
   {

   lcd.setCursor(0,1);
    lcd.print("Temperature:");
    lcd.print(temp);
   delay(3000);
    if(count == 0)
     {
      count++;
        dijkstra(graph, s,d);

   }
 }

   else
   {
    lcd.setCursor(0,1);
    lcd.print("Temperature:");
    lcd.print(temp);
   }

  delay(3000);

}